## Slide 1
GHS
The Globally Harmonized System of Classification and Labeling of Chemicals
Notes: <number>

## Slide 2
Part of the Hazard Communication Standard
Consistent System of Classification and Labeling of Chemicals
Created by the United Nations
What is GHS?
Notes: GHS is a part of the Right to Know standard also known as Hazard Communication or Haz-Comm. It is a system of classifying and labeling chemicals that was created by the UN in 1992 during the United Nations Conference on Environment and Development as part of Agenda 21. The international standard was created to ensure import and export of chemicals was consistent in all member nations and to assist developing nations in creating standards.
Federal OSHA says, “Chemicals directly or indirectly affect our lives and are essential to our food, our health, and our lifestyle. The widespread use of chemicals has resulted in the development of sector-specific regulations (transport, production, workplace, agriculture, trade, and consumer products). Having readily available information on the hazardous properties of chemicals, and recommended control measures, allows the production, transport, use and disposal of chemicals to be managed safely. Thus, human health and the environment are protected. The sound management of chemicals should include systems through which chemical hazards are identified and communicated to all who are potentially exposed. These groups include workers, consumers, emergency responders and the public. It is important to know what chemicals are present and/or used, their hazards to human health and the environment, and the means to control them. A number of classification and labeling systems, each addressing specific use patterns and groups of chemicals, exist at the national, regional and international levels”
<number>

## Slide 3
Notes: All state OSHA plans also adopted the standard in order to maintain the global system. Oregon adopted it on September 25, 2012 and made the rules effective on the same date.
<number>

## Slide 4
Oregon OSHA’s phase-in dates under the revised Hazard Communication Standard (HCS):
Chemical manufacturers, importers, distributors, and employers
May comply with either 29 CFR 1910.1200 (the final standard), or the current standard, or both.
Transition Period to the effective completion dates noted above
Employers
Update alternative workplace labeling and hazard communication program as necessary, and provide additional employee training for newly identified physical or health hazards.
June 1, 2016
Chemical manufacturers, importers, distributors and employers
Compliance with all modified provisions of this final rule, except: The Distributor shall not ship containers labeled by the chemical manufacturer or importer unless it is a GHS label.
June 1, 2015 December 1, 2015
Employers
Train employees on the new label elements and safety data sheet (SDS) format.
December 1, 2013
Who
Requirement(s)
Effective Completion Date
FOR MORE INFORMATION
PLEASE VISIT OSHA’s WEBSITES:
http://orosha.org/subjects/hazard_communication.html
www.osha.gov/dsg/hazcom/index.html
Notes: There are four important implementation dates to be aware of. December 1, 2013; June 1, 2015; December 1, 2015; and June 1, 2016.
The first implementation date of December 1, 2013 relates to the requirement for employers to have a discussion with their employees about the changes in the haz comm standard. The employer must provide training to their employees on SDS and the new labels.
<number>

## Slide 5
Changes of the Standard:
Labels
Pictograms
Safety Data Sheets
Hazard Classification vs. Identification
Notes: The changes will center on these areas of hazard communication. Labels, Pictograms, Safety Data Sheets and the way hazards are looked at on the Safety Data Sheets.
<number>

## Slide 6
http://www.osha.gov/dsg/hazcom/ghsquickcards.html
One way to get information are OSHA’s Quick Cards:
Notes: A simple way to do this training is with the Federal OSHA quick cards. You can obtain them by visiting www.osha.gov and selecting hazard communication from the A-Z topic listing.
<number>

## Slide 7
LABELS
Notes: OSHA has updated the requirements for labeling of hazardous chemical under its Hazard Communication Standard (HCS). As of June 1, 2015, all labels will be required to have pictograms, a signal word, hazard and precautionary statements, the product identifier, and supplier identification. A sample revised HCS label, identifying the required label elements, is shown on the right. Supplemental information can also be provided on the label as needed.
<number>

## Slide 8
PICTOGRAMS
Notes: As of June 1, 2015, the Hazard Communication Standard (HCS) will require pictograms on labels to alert users of the chemical hazards to which they may be exposed. Each pictogram consists of a symbol on white background frames within a red border and represents a distinct hazard(s). The pictogram on the label is determined by the chemical hazard classification.
<number>

## Slide 9
Section 1 Identification
Section 2 Hazard(s) identification
Section 3 Composition/information on ingredients
Section 4 First-aid measures
Section 5 Fire-fighting measures
Section 6 Accidental release measures
Section 7 Handling and storage
Section 8 Exposure controls/personal protection
Section 9 Physical and chemical properties
Section 10 Stability and reactivity
Section 11 Toxicological information
Section 12 Ecological information*
Section 13 Disposal considerations*
Section 14 Transport information*
Section 15 Regulatory information*
Section 16 Other information
SAFETY DATA SHEETS
Notes: New data sheets will now contain 16 sections. The sections will follow this outline.
<number>

## Slide 10
Section 1, Identification
Section 2, Hazard(s) identification
SAFETY DATA SHEETS
Notes: The Hazard Communication Standard (HCS) requires chemical manufacturers, distributors, or importers to provide Safety Data Sheets (SDSs) (formerly know as Material Safety Data Sheets or MSDSs) to communicate the hazards of chemical products. As of June 1, 2015, the HCS will require new SDSs to be in a uniform format, and include the section numbers, the headings, and associated information under the headings below:
Section 1, Identification
includes product identifier; manufacturer or distributor name, address, phone, number; recommended use; restriction on use.
Section 2, Hazard(s) identification
includes all hazards regarding the chemical; required label elements.
<number>

## Slide 11
Section 3, Composition/information on ingredients
Section 4, First-aid measures
Section 5, Fire-fighting measures
SAFETY DATA SHEETS
Notes: Section 3, Composition/information on ingredients
includes information on chemical ingredients; trade secret claims.
Section 4, First-aid measures
includes important symptoms/effects, acute, delayed; required treatment.
Section 5, Fire-fighting measures
lists suitable extinguishing techniques, equipment; chemical hazards from fire.
<number>

## Slide 12
Section 6, Accidental release measures
Section 7, Handling and storage
Section 8, Exposure controls/personal protection
SAFETY DATA SHEETS
Notes: Section 6, Accidental release measures
lists emergency procedures; protective equipment; proper methods of containment and cleanup.
Section 7, Handling and storage
lists precautions for safe handling and storage, including incompatibilities.
Section 8, Exposure controls/personal protection
lists OSHA’s Permissible Exposure Limits (PELs); Threshold Limit Values (TLVs); appropriate engineering controls; personal protective equipment (PPE).
<number>

## Slide 13
Section 9, Physical and chemical properties
Section 10, Stability and reactivity
Section 11, Toxicological information
SAFETY DATA SHEETS
Notes: Section 9, Physical and chemical properties
lists the chemical's characteristics.
Section 10, Stability and reactivity
lists chemical stability and possibility of hazardous reactions.
Section 11, Toxicological information
includes routes of exposure; related symptoms, acute and chronic effects; numerical measures of toxicity.
<number>

## Slide 14
Section 12, Ecological information*
Section 13, Disposal considerations*
Section 14, Transport information*
Section 15, Regulatory information*
Section 16, Other information, includes the date of preparation or last revision.
OSHA will not be enforcing Sections 12 through 15
SAFETY DATA SHEETS
Notes: Since other Agencies regulate this information, OSHA will not be enforcing Sections 12 through 15 (29 CFR 1910.1200(g)(2).
Employers must ensure that SDSs are readily accessible to employees.
See Appendix D of 29 CFR 1910.1200 for a detailed description of SDS contents.
<number>

## Slide 15: Hazard Identification vs. Hazard Classification
Notes: The chemical manufacturers will be providing this information
<number>

## Slide 16
May cause skin and severe eye irritation.
Harmful if swallowed.
May cause severe irritation of gastric mucous membranes if swallowed.
Prolonged contact with skin may whiten skin and cause burns.
Decomposition yields oxygen and may support combustion.
Hazard Identification - MSDS
L’Oreal USA Products, Inc. PRODUCT: 0-25 Volume Developer
≥ 8% Hydrogen Peroxide (June 22. 2009)
Notes: Both current Hazard Communication Standard (HCS) and the revised HCS require an evaluation of chemical hazards. Under current HCS the hazard determination provisions have definitions of hazard and the evaluator determines whether or not the data on a chemical meet those definitions. (Performance based). The current HCS does not include categories for most of the health hazards covered, so this new approach provides additional information that can be related to the appropriate response to address the hazard.
<number>

## Slide 17
Hazard Classification - SDS
Classification | Hazard Statement | Prevention Statements
Serious Eye Damage Category 1 | Causes serious eye damage | Wear eye protection/face protection. Chemical resistant goggles or a face shield is appropriate for the manufacturing environment. Wash hands and face thoroughly after handling.
Oxidizing Liquid Category 3 | May intensify fire, oxidizer | Keep away from heat. Storage away from combustibles (e.g. paper), organics, and metals (e.g. Iron). Take precaution to avoid mixing with combustible and organic materials. Wear protective glovers and ye/face protection when in the manufacturing environment.
L’Oreal USA Products, Inc. PRODUCT: 0-25 Volume Developer
≥ 8% Hydrogen Peroxide (July 17, 2012)
Harmful if swallowed. Overexposure may cause skin dryness or slight irritation. Prolonged contact may whiten skin. May cause irritation of gastric mucous membranes if swallowed.
Notes: The revised HCS has specific criteria for each health and physical hazard, along with detailed instructions for hazard evaluation and determinations as to whether mixtures or substances are covered. (Criteria based). The revised HCS establishes both hazard classes and hazard categories—for most of the effects; the classes are divided into categories that reflect the relative severity of the effect.
OSHA has included the general provisions for hazard classification in paragraph (d) of the revised rule, and added extensive appendixes (Appendixes A and B) that address the criteria for each health or physical effect.
<number>

## Slide 18
For more information:
http://orosha.org/subjects/hazard_communication.html
Notes: For more information:
http://orosha.org/subjects/hazard_communication.html
<number>